Rugby union pitch: budget costs  Protecting Playing Fields Programme

| Important Note: Costs shown are typical budget costs to support applications to the Protecting Playing Fields Programme and should not be used for other purposes. The actual cost for any site will only be known after a full site appraisal, the production of a detailed specification, bill of quantities, drawings and receipt of tender bids for the proposed works. * The pitch sizes provided are the MAXIMUM size for that age group * If your pitch size isn’t listed opposite, please choose the one closest the size of your pitch * If you already have a site survey or Feasibility Study with costs for your project then please use them in your application. * Costs are exclusive of VAT | Adult 100 x 70 m with 22 m dead ball lines and 5 m safety margin on all sides. | Junior (U11-U12) 60 x 43 m with 5 m dead ball lines and 5m safety margin on all sides. |
| --- | --- | --- |
| Piped drainage scheme with sand grooves (if required) Typical costs include preliminaries, setting up, transport, installation of pipe drainage scheme, installation of sand grooves, application of fertilizer, seeding and making good1,2. Budget cost for piped drainage with sand grooves | £57,500 | £24,500 |
| Re-grading and improvement of playing surface (if required) Typical costs include preliminaries, setting up, transport, removal of vegetation and goal post sockets, top soil importation, cultivation and grading, sand amelioration, applying fertilizer, seeding and reinstatement3. Budget cost for regrading and surface improvement | £37,800 | £15,000 |
| Initial maintenance following drainage or improvement works (12 months, provided by the pitch contractor) On completion of improvement works, natural turf pitches are rarely in a condition that would allow them to be playable as the grass will be immature and susceptible to damage. It is therefore recommended that the contractor is responsible for ‘growing-in’ the pitch and maintaining it for 12 months. Typical costs include mowing, fertilizer and herbicide application, applying and working in topdressing sand, overseeding, compaction alleviation and the treatment of pests and diseases. Budget cost for initial maintenance (12 months) | £28,900 | £10,500 |
| Annual grounds maintenance costs (assumes all operations are contracted out) It is critical to the long term success of any new pitch works that the pitch is properly maintained. Maintenance work should be carried out by experienced groundsmen and will typically incorporate the following: mowing (say 30 cuts/annum), spreading fertilizer, applying herbicide, applying and working in top dressing sand, reseeding, compaction alleviation, spiking/slitting (x4), application of pesticide/fungicide, weekly line marking and scarification. For clubs using their own volunteers or staff, the costs of maintenance may be lower. Budget cost for regular ongoing maintenance | £19,000 | £7,500 |

For situations where the outfall for the drainage water (e.g. a nearby ditch, stream or manhole) is higher than the piped drainage system, there will be a need to install a sump with a pump so that water can be pumped up to the outfall.  Pump and sump systems typically add £8,000 to £12,000 to the drainage costs.

In certain circumstances, a restriction may be placed on the amount of drainage water that can leave the site in a given time, necessitating the design and installation of some form of attenuation system.  These are commonly referred to as sustainable urban drainage systems (SUDS) and typically add £4,000 to £8,000 to the drainage costs.

In exceptional circumstances where the slope of the pitch is excessive, it may be necessary to remove the topsoil, reshape the subsoil by removing high areas and building up low areas, replace the topsoil and reseed the site.  Depending on how much re-modelling is required, this can add between 20 and 30 % to the re-grading and improvement of playing surface cost.